## Slide 1: logic circuits

## Slide 2
perform operations on digital signals
Implemented as electronic circuits where signal values are restricted to a few discrete values
In binary logic circuits there are only two values, 0 and 1
The general form of a logic circuit is a switching network

## Slide 3: Boolean algebra
Direct application to switching networks
Work with 2-state devices i.e 2-valued Boolean algebra (switching algebra)
Use a Boolean variable (X, Y, etc.) to represent an input or output of a switching network
Variable may take on only two values (0, 1)
    X=0, X=1
These symbols are not binary numbers, they simply represent the 2 states of a Boolean variable
They are not voltage levels, although they commonly refer to the low or high voltage input/output of some circuit element

## Slide 4: Variables and functions
The simplest binary element is a switch that has two states
If the switch is controlled by x, we say the switch is open if x =0 and closed if x =1

## Slide 5: Variables and functions

## Slide 6
Assume the switch controls a lightbulb as shown, The output is defined as the state of the light L
    If the light is on -> L=1
    If the light is off -> L=0
    Refer to image on next slide
The state of L, as a function of x is
  L(x)=x
  L(x) is a logic function
  x is an input variable

## Slide 7: Variables and functions

## Slide 8: Variables and functions (AND)
Consider the possibility of two switches controlling the state of the light
Using a series connection, the light will be on only if both switches are closed
    L(x1, x2)= x1· x2
    L=1 iff (if and only if) x1 AND x2 are 1
The circuit implements a logical AND function

## Slide 9: Variables and functions (AND)

## Slide 10: Variables and functions (OR)
Using a parallel connection, the light will be on only if either or both switches are closed
    L(x1, x2)= x1+ x2
    L=1 if x1 OR x2 is 1 (or both)
The circuit implements a logical OR function

## Slide 11: Variables and functions (OR)

## Slide 12
Various series-parallel connections would realize various logic functions
Example;
  L(x1, x2, x3)= (x1 + x2) · x3

## Slide 13: Series-parallel

## Slide 14: Inversion
Before, actions occur when a switch is closed.
What about the possibility of an action occurring when a switch is opened?
  L(x)= x’
  Where L=1 if x=0 and L=0 if x=1
  L(x) is the inverse (or complement) of x
The circuit implements a logical NOT function

## Slide 15: Inversion

## Slide 16: Inversion of a function
If a function is defined as f(x1, x2)= x1+ x2
  Then the complement of f is
  f’(x1, x2)= x’1+ x’2 = (x1+ x2)’
Similarly, if f(x1, x2)= x1 · x2
  Then the complement of f is
  f’(x1, x2)= x1’ · x2’= (x1 · x2)’

## Slide 17: Logic gates and networks
Each basic logic operation (AND, OR, NOT) can be implemented resulting in a circuit element called a logic gate
A logic gate has one or more inputs and one output that is a function of its inputs
A larger circuit is implemented by a network of gates– Called a logic network or logic circuit

## Slide 18: Logic gates and networks (AND, OR)

## Slide 19: Logic gates and networks (NOT, LOGIC CIRCUIT)