## Slide 1
Zhang Linrui/zwx570554

## Slide 2: Network Management and O&M

## Slide 3
The ever expanding network and increasing network devices present a significant challenge in managing networks effectively and providing high-quality network services.
There are many network management and O&M methods, of which this course describes some of the most common.

## Slide 4
On completion of this course, you will be able to:
  Understand basic concepts of network management and O&M.
  Master common network management and O&M methods.
  Describe basic functions of network management and O&M.
  Understand the fundamentals of SNMP.
  Understand Huawei iMaster NCE and related technologies.

## Slide 5
Basic Concepts of Network Management and O&M
SNMP Fundamentals and Configuration
Network Management Based on Huawei iMaster NCE

## Slide 6: What Is Network Management and O&M?
Network management and O&M plays an important role on a communications network. It ensures that devices work properly and the communications network runs properly to provide efficient, reliable, and secure communications services.
Common enterprise network architecture
Network administrator
The network administrator manages and maintains the network for stable operation.
Notes: Network management and O&M is classified as software management or hardware management.
  Software management: management of network applications, user accounts (such as accounts for using files), and read and write permissions. This course does not describe software management in detail.
  Hardware management: management of network elements (NEs) that constitute the network, including firewalls, switches, routers, and other devices. This course mainly describes hardware management.
Generally, an enterprise network has dedicated departments or personnel responsible for network management and O&M.
Note:
  A network element (NE) refers to a hardware device and software running on the hardware device. An NE has at least one main control board that manages and monitors the entire NE. The NE software runs on the main control board.

## Slide 7: Basic Network Management Functions
OSI defines five functional models for network management:
  Configuration management: monitors network configuration information so that network administrators can generate, query, and modify hardware and software running parameters and conditions, and configure services.
  Performance management: manages network performance so that the network can provide reliable, continuous, and low-latency communication capabilities with as few network resources as possible.
  Fault management: ensures that the network is always available and rectifies faults as soon as possible.
  Security management: protects networks and systems from unauthorized access and attacks.
  Accounting management: records the network resource usage of users, charges users, and collects statistics on network resource usage.
Configuration
management
Performance
management
Fault
management
Security
management
Accounting
management

## Slide 8: Network Management Modes
Network administrator
Network management station
Web system
mode
CLI
mode
SNMP-based
centralized management
Traditional Network Management and O&M
ERP
Network
automation
Network
intelligence
`
Cloud platform
Northbound API
Commercial application
iMaster NCE
Data center
Campus
WAN
Branch
Video conferencing
Advertisement operations
Office OS
Analysis
Management
Control
iMaster NCE-based Network Management and O&M
Notes: Traditional network management:
  Web system: The built-in web server of the device provides a graphical user interface (GUI). You need to log in to the device to be managed from a terminal through Hypertext Transfer Protocol Secure (HTTPS).
  CLI mode: You can log in to a device through the console port, Telnet, or SSH to manage and maintain the device. This mode provides refined device management but requires that users be familiar with command lines.
  SNMP-based centralized management: The Simple Network Management Protocol (SNMP) provides a method for managing NEs (such as routers and switches) by using a central computer (that is, a network management station) that runs network management software. This mode provides centralized and unified management of devices on the entire network, greatly improving management efficiency.
iMaster NCE-based network management:
  iMaster NCE is a network automation and intelligence platform that integrates management, control, analysis, and AI functions. It provides four key capabilities: full-lifecycle automation, intelligent closed-loop management based on big data and AI, scenario-specific app ecosystem enabled by open programmability, and all-cloud platform with ultra-large system capacity.
  iMaster NCE uses protocols such as Network Configuration Protocol (NETCONF) and RESTCONF to deliver configurations to devices and uses telemetry to monitor network traffic.

## Slide 9
Basic Concepts of Network Management and O&M
Traditional Network Management
Network Management Based on Huawei iMaster NCE

## Slide 10: Management Through the CLI or Web System
When the network scale is small, the CLI and web system are generally used for network management.
  Network administrators can log in to a device through HTTPS, Telnet, or the console port to manage the device.
  These network management modes do not require any program or server to be installed on the network, and the cost is low.
  Network administrators must have a good master of network knowledge and vendor-specific network configuration commands.
  These modes have great limitations when the network scale is large and the network topology is complex.
Network administrator
One-to-one management
Vendor A
Switch
Vendor A
Firewall
Vendor A
AC
Vendor A
Router
Vendor B
Router
Vendor C
Switch
Vendor D
Switch
Notes: As networks rapidly expand and applications become more diversified, network administrators face the following problems:
  The fast growth of network devices increases network administrators' workloads. In addition, networks' coverage areas are constantly being expanded, making real-time monitoring and fault locating of network devices difficult.
  There are various types of network devices and the management interfaces (such as command line interfaces) provided by different vendors vary from each other, making network management more complex.

## Slide 11: SNMP-based Centralized Management
SNMP is a standard network management protocol widely used on TCP/IP networks. It provides a method for managing NEs through a central computer that runs network management software, that is, a network management station.
NMS
Network administrator
SNMP
packet exchange
One-to-many management
Network administrators can use the NMS to query information, modify information, and troubleshoot faults on any node on the network, improving work efficiency.
Network devices of different types and vendors are managed in a unified manner.
Notes: There are three SNMP versions: SNMPv1, SNMPv2c, and SNMPv3.
  In May 1990, RFC 1157 defined the first SNMP version: SNMPv1. RFC 1157 provides a systematic method for monitoring and managing networks. SNMPv1 implements community name-based authentication, failing to provide high security. In addition, only a few error codes are returned in SNMPv1 packets.
  In 1996, the Internet Engineering Task Force (IETF) released RFC 1901 in which SNMPv2c is defined. SNMPv2c provides enhancements to standard error codes, data types (Counter 64 and Counter 32), and operations including GetBulk and Inform.
  SNMPv2c still lacks security protection measures, so IETF released SNMPv3. SNMPv3 provides user security module (USM)-based encryption and authentication and a view-based access control model (VACM).

## Slide 12: Typical SNMP Architecture
On a network where SNMP is used for network management, a network management system (NMS) functions as a network management center and runs management processes. Each managed device needs to run an agent process. The management process and agent process communicate with each other through SNMP messages.
An NMS is a system that uses SNMP to manage and monitor network devices. The NMS software runs on NMS servers.
Managed devices are devices that are managed by the NMS on the network.
The agent process runs on managed devices to maintain the information data of the managed devices, respond to the request from the NMS, and report the management data to the NMS that sends the request.
Network management process
NMS
Client
Monitor
Provides a visualized interface.
SNMP message
Agent process
Managed device
Agent process
Managed device
IP Network
Agent process
Managed device
Notes: An NMS is an independent device that runs network management programs. The network management programs provide at least one man-machine interface for network administrators to perform network management operations. Web page interaction is a common man-machine interaction mode. That is, a network administrator uses a terminal with a monitor to access the web page provided by the NMS through HTTP/HTTPS.

## Slide 13: SNMP Message Exchange
The NMS and managed devices exchange messages in the following modes:
  The NMS sends a request for modifying or querying configuration information to a managed device through SNMP. The agent process running on the managed device responds to the request from the NMS.
  The managed device can proactively report traps to the NMS so that the network administrator can detect faults in a timely manner.
Managed object: Each device may contain multiple managed objects. A managed object can be a hardware component or a set of parameters configured on the hardware or software (such as a routing protocol).
SNMP uses management information bases (MIBs) to describe a group of objects of a manageable entity.
Managed object
Network management process
NMS
Agent process
Managed device
Query/Modify Request
Query/Modify response
Trap
1
2
3

## Slide 14: MIB
A MIB is a database containing the variables that are maintained by managed devices. (The variables can be queried or set by the agent processes.) The MIB defines the attributes of managed devices in the database.
  Object identifier (OID) of an object
  Status of an object
  Access permission of an object
  Data types of an object
A MIB provides a structure that contains data on all NEs that may be managed on the network. Because the data structure is similar to the tree structure, a MIB is also called an object naming tree.
root
iso (1)
ccitt (0)
joint-iso-ccitt (2)
org (3)
dod (6)
internet (1)
mgmt (2)
mib (1)
system (1)
interface (2)
...
...
...
OID:1.3.6.1.2
Notes: MIB is defined independently of a network management protocol. Device vendors can integrate SNMP agent software into their products (for example, routers), but they must ensure that this software complies with relevant standards after new MIBs are defined. You can use the same network management software to manage routers containing MIBs of different versions. However, the network management software cannot manage a router that does not support the MIB function.
There are public MIBs and private MIBs.
  Public MIBs: defined by RFCs and used for structure design of public protocols and standardization of interfaces. Most vendors need to provide SNMP interfaces according to the specifications defined in RFCs.
  Private MIBs: They are the supplement of the public MIBs. Some enterprises need to develop private protocols or special functions. The private MIBs are designed to enable the SNMP interface to manage such protocols or functions. They also help the NMS provided by the third party to manage devices. For example, the MIB object of Huawei is 1.3.6.1.4.1.2011.

## Slide 15: Common MIB Objects
Objects used for query or modification:
Objects used for alarm notification:
OID | Object Name | Data Type | Maximum Access | Description
1.3.6.1.2.1.2.1 | ifNumber | Integer | read-only | Number of network interfaces in the system (regardless of the current interface status)
1.3.6.1.4.1.2011.5.25.41.1.2.1.1.3 | hwIpAdEntNetMask | IpAddress | read-create | Subnet mask of an IP address
OID | Object Name | Bound Variable | Description
3.6.1.6.3.1.1.5.3 | linkDown | ifIndex ifAdminStatus ifOperStatus ifDesc | It is detected that one of the communication links in the ifOperStatus object has entered the down state from another state (but not the notPresent state). The original state is indicated by the value of ifOperStatus.
Notes: The maximum access permission of a MIB object indicates the operations that the NMS can perform on the device through the MIB object.
  not-accessible: No operation can be performed.
  read-only: reads information.
  read-write: reads information and modifies configurations.
  read-create: reads information, modifies configurations, adds configurations, and deletes configurations.
When generating a trap, the device reports the type of the current trap together with some variables. For example, when sending a linkDown trap, the device also sends variables such as the interface index and current configuration status of the involved interface.
  ifIndex: interface index (number)
  ifAdminStatus: indicates the administrative status, that is, whether the interface is shut down. 1 indicates that the interface is not shut down, and 2 indicates that the interface is shut down.
  ifOperStasuts: indicates the current operating status of the interface, that is, the link layer protocol status of the interface. The value 1 indicates Up, 2 indicates Down.
  ifDesc: interface description

## Slide 16: SNMP Management Model
Query/Modify operation:
  The NMS sends an SNMP request message to an agent process.
  The agent process searches the MIB on the device for information to be queried or modified and sends an SNMP response message to the NMS.
Trap operation:
  If the trap triggering conditions defined for a module are met, the agent process sends a message to notify the NMS that an event or trap has occurred on a managed object. This helps network administrators promptly process network faults.
Network management process
NMS
Agent process
Managed devices
MIB
Managed object
SNMP message exchange

## Slide 17: SNMPv1
NMS
Managed device
Get
What's the IP address
of GE 0/0/1
GetNext
What's the IP address
of GE 0/0/2
Set
Set the IP address of
GE 0/0/3 to 10.0.3.1/24.
Response
10.0.1.1/24
Response
10.0.2.1/24
Response
Setting succeeded.
Trap
The CPU usage is too high.
IP Network
Notes: SNMPv1 defines five protocol operations.
  Get-Request: The NMS extracts one or more parameter values from the MIB of the agent process on the managed device.
  Get-Next-Request: The NMS obtains the next parameter value from the MIB of the agent process in lexicographical order.
  Set-Request: The NMS sets one or more parameter values in the MIB of the agent process.
  Response: The agent process returns one or more parameter values. It is the response to the first three operations.
  Trap: The agent process sends messages to the NMS to notify the NMS of critical or major events.

## Slide 18: SNMPv2c
NMS
Managed device
Get
GetNext
Set
Response
Response
Response
Trap
GetBulk
Query the IP addresses of
all interfaces on the device
Inform
The CPU usage is too high.
Response
Alarm received.
Response
The IP address of GE 0/0/1 is...
The IP address of GE 0/0/2 is...
IP Network
Notes: SNMPv2c supports the following operations:
  GetBulk: equals to multiple GetNext operations. You can set the number of GetNext operations to be included in one GetBulk operation.
  Inform: A managed device proactively sends traps to the NMS. In contrast to the trap operation, the inform operation requires an acknowledgement. After a managed device sends an InformRequest message to the NMS, the NMS returns an InformResponse message. If the managed device does not receive the acknowledgment message, it temporarily saves the trap in the Inform buffer and resends the trap until the NMS receives the trap or the number of retransmission times reaches the maximum.

## Slide 19: SNMPv3
SNMPv3 has the same working mechanism as SNMPv1 and SNMPv2c, but adds header data and security parameters.
SNMPv3 messages can be authenticated and encrypted.
SNMPv3 is applicable to networks of various scales and has high security.
NMS
Managed device
Authenticates all exchanged messages
and encrypts messages.
IP Network
Notes: SNMPv3 supports identity authentication and encryption.
  Identity authentication: A process in which the agent process (or NMS) confirms whether the received message is from an authorized NMS (or agent process) and whether the message is changed during transmission.
  Encryption: The header data and security parameter fields are added to SNMPv3 messages. For example, when the management process sends an SNMPv3 Get-Request message carrying security parameters such as the username, key, and encryption parameters, the agent process also uses an encrypted response message to respond to the Get-Request message. This security encryption mechanism is especially applicable to a scenario in which data needs to be transmitted through a public network between the management process and agent process.

## Slide 20: SNMP Summary
SNMP has the following advantages:
  Simplicity: SNMP is applicable to networks that require high speed and low cost because it uses a polling mechanism and provides basic network management functions. Moreover, SNMP uses UDP to exchange data and therefore is supported by most products.
  Convenience: SNMP allows management information exchange between arbitrary devices on a network, so that a network administrator can query information and locate faults on any device.
SNMPv1 applies to small-scale networks where security requirements are not high or the network environment is safe and stable, such as campus networks and small-sized enterprise networks.
SNMPv2c applies to medium- and large-sized networks where security requirements are not high or the network environment is safe, but a large volume of traffic exists and traffic congestion may occur.
SNMPv3 is the recommended version and applies to networks of various scales, especially those networks that have high security requirements and allow only authorized administrators to manage network devices.

## Slide 21: Basic SNMP Configuration (1)
[Huawei] snmp-agent
Enable the SNMP agent function.
[Huawei] snmp-agent sys-info version [v1 | v2c | v3]
Set the SNMP version.
[Huawei] snmp-agent group v3 group-name { authentication | noauth | privacy } [ read-view view-name | write-view view-name | notify-view view-name ]
Create or update MIB view information.
You can configure the SNMP version as required. However, the protocol version used on the device must be the same as that used on the NMS.
4. Add a new SNMP group and map users in this group to the SNMP view.
[Huawei] snmp-agent mib-view view-name { exclude | include } subtree-name [mask mask]
This command is used to create an SNMP group of the SNMPv3 version and specify the authentication and encryption mode and one or more of read-only view, read-write view, and notification view. It is a mandatory command on networks that require high security.

## Slide 22: Basic SNMP Configuration (2)
6. Configure an authentication password for an SNMPv3 user.
[Huawei] snmp-agent usm-user v3 user-name authentication-mode { md5 | sha | sha2-256 }
[Huawei] snmp-agent usm-user v3 user-name privacy-mode { aes128 | des56 }
7. Configure the SNMPv3 user encryption password.
[Huawei] snmp-agent usm-user v3 user-name group group-name
5. Add a user to the SNMP group.
[Huawei] snmp-agent target-host trap-paramsname paramsname v3 securityname securityname { authentication | noauthnopriv | privacy }
8. Set parameters for the device to send traps.

## Slide 23: Basic SNMP Configuration (3)
10. Enable all trap functions.
[Huawei] snmp-agent trap enable
[Huawei] snmp-agent trap source interface-type interface-number
11. Configure the source interface that sends traps.
Note that this command is used only to enable the device to send traps. This command must be used together with the snmp-agent target-host command. The snmp-agent target-host command specifies the device to which traps are sent.
[Huawei] snmp-agent target-host trap-hostname hostname address ipv4-address trap-paramsname paramsname
9. Configure the target host of traps.
Note that a source IP address must have been configured for the interface that sends traps.

## Slide 24: SNMP Configuration Example (Network Device Side)
NMS
Managed device
192.168.1.10
GE0/0/1
R1configuration:
[R1]snmp-agent
[R1]snmp-agent sys-info version v3
[R1]snmp-agent group v3 test privacy
[R1]snmp-agent usm-user v3 R1 test authentication-mode md5 HCIA@Datacom123 privacy-mode aes128 HCIA-Datacom123
[R1]snmp-agent target-host trap-paramsname param v3 securityname sec privacy
[R1]snmp-agent target-host trap-hostname nms address 192.168.1.10 trap-paramsname param
[R1]snmp-agent trap source GigabitEthernet 0/0/1
[R1]snmp-agent trap enable
Info: All switches of SNMP trap/notification will be open. Continue? [Y/N]:y
R1
Enable SNMP on R1and set the SNMP version to SNMPv3.
Set the SNMPv3 group name to test and encryption authentication mode to privacy.
Create an SNMPv3 user named R1 and set the authentication and encryption passwords to HCIA-Datacom123.
Create a trap parameter named param and set securityname to sec.
Set the IP address of the SNMP target host to 192.168.1.10.
Enable the trap function and specify GE 0/0/1 as the source interface that sends traps.

## Slide 25
Basic Concepts of Network Management and O&M
Traditional Network Management
Network Management Based on Huawei iMaster NCE

## Slide 26: Transformation and Challenges of the Network Industry
With the advent of the 5G and cloud era, innovative services such as VR/AR, live streaming, and autonomous driving are emerging, and the entire ICT industry is booming. At the same time, the traffic of the entire network also increases explosively. Huawei Global Industry Vision (GIV) predicts that the amount of new data will reach 180 ZB by 2025. Moreover, the dynamic complexity of services makes the entire network more complex.
Such challenges can only be overcome by constructing automated and intelligent network systems centered on user experience.
Autonomous driving
VR/AR
Live streaming
Traditional networks are overloaded.
Notes: One zettabyte (abbreviated "ZB") is equal to 1012 GB.

## Slide 27: Huawei iMaster NCE
Huawei iMaster NCE is a network automation and intelligence platform that integrates management, control, analysis, and AI functions.
In terms of management and control, iMaster NCE allows you to:
  Manage and control traditional devices through traditional technologies such as CLI and SNMP.
  Manage and control SDN-capable networks through NETCONF (based on the YANG model).
iMaster NCE collects network data through protocols such as SNMP and telemetry, performs intelligent big data analysis based on AI algorithms, and displays device and network status in multiple dimensions through dashboards and reports, helping O&M personnel quickly detect and handle device and network exceptions and ensuring normal running of devices and networks.
Telemetry
Traditional devices
SDN-capable network devices
NETCONF/YANG
CLI/SNMP
Unified cloud-based platform
Management
Control
Analysis
iMaster NCE
Open API
Intent engine
Cloud platform & application
Notes: iMaster NCE provides the following key capabilities:
  Full-lifecycle automation: iMaster NCE provides full-lifecycle automation across multiple network technologies and domains based on unified resource modeling and data sharing, enabling device plug-and-play, immediate network availability after migration, on-demand service provisioning, fault self-healing, and risk warning.
  Intelligent closed-loop management based on big data and AI: iMaster NCE constructs a complete intelligent closed-loop system based on its intent engine, automation engine, analytics engine, and intelligence engine. It also uses telemetry to collect and aggregate massive volumes of network data. This allows it to determine the network status in real time. iMaster NCE provides big data-based global network analysis and insights through unified data modeling, and is equipped with Huawei's sophisticated AI algorithms accumulated during its 30 years in the telecom industry. It provides automated closed-loop analysis, forecast, and decision-making based on customers' intents. This helps improve user experience and continuously enhance network intelligence.

## Slide 28
Notes:   Open programmability-enabled scenario-based application ecosystem: In the southbound direction, iMaster NCE provides a programmable integrated development environment — Design Studio — and a developer community for integration with third-party network controllers and devices; in the northbound direction, it provides cloud-based AI training platforms and IT applications. iMaster NCE allows customers to purchase Huawei native apps on demand, develop their own apps, and turn to third-party system integrators for app development.
  Large-capacity cloud platform: iMaster NCE, with cloud-native architecture, supports both on-premises deployment and cloud-based deployment. With elastic scalability, it can provide large system capacity to allow a large number of access users. With online data sharing and process streamlining, it avoids scattered data distribution and multi-level O&M in offline mode.

## Slide 29: NETCONF Overview
NETCONF provides a network device management mechanism. You can use NETCONF to add, modify, or delete configurations of network devices, and obtain configurations and status of network devices.
NETCONF server
Device
Device 1
Device 2
Device 3
Network
NETCONF client
NETCONF message exchange
NETCONF has three objects:
NETCONF client
NETCONF server
NETCONF message
NETCONF requires that messages exchanged between a client and server be encoded using XML.
Notes: NETCONF client: manages network devices using NETCONF. Generally, the NMS functions as the NETCONF client. It sends <rpc> elements to a NETCONF server to query or modify configuration data. The client can learn the status of a managed device based on the traps and events reported by the server.
NETCONF server: maintains information about managed devices, responds to requests from clients, and reports management data to the clients. NETCONF servers are typically network devices, for example, switches and routers. After receiving a request from a client, a server parses data, processes the request with the assistance of the Configuration Manager Frame (CMF), and then returns a response to the client. If a trap is generated or an event occurs on a managed device, the NETCONF server reports the trap or event to the client through the Notification mechanism, so the client can learn the status change of the managed device.
A client and a server establish a connection based on a secure transmission protocol such as Secure Shell (SSH) or Transport Layer Security (TLS), and establish a NETCONF session after exchanging capabilities supported by the two parties using Hello packets. In this way, the client and the server can exchange messages. A network device must support at least one NETCONF session. The data that a NETCONF client obtains from a NETCONF server can be configuration data or status data.

## Slide 30: NETCONF Advantages
Function | NETCONF | SNMP | CLI
Interface type | Machine-machine interface: The interface definition is complete and standard, and the interface is easy to control and use. | Machine-to-machine interface | Man-machine interface
Operation efficiency | High: Object-based modeling is supported. Only one interaction is required for object operations. Operations such as filtering and batch processing are supported. | Medium | Low
Scalability | Proprietary protocol capabilities can be extended. | Weak | Moderate
Transaction | Supports transaction processing mechanisms such as trial running, rollback upon errors, and configuration rollback. | Not supported | Partially supported
Secure transmission | Multiple security protocols: SSH, TLS, BEEP/TLS, and SOAP/HTTP/TLS | Only SNMPv3 supports secure transmission. | SSH

## Slide 31: Typical NETCONF Interaction
<?xml version="1.0" encoding="UTF-8"?>
<rpc xmlns="urn:ietf:params:xml:ns:netconf:base:1.0" message-id= "101">
<edit-config>
<target>
<running/>
</target>
<config>
Configuration content in XML format
</config>
</edit-config>
</rpc>
This operation is to modify configuration.
<?xml version="1.0" encoding="UTF-8"?>
<rpc-reply message-id="101" xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<ok/>
</rpc-reply>
RPC
SSH connection
RPC-Reply
Modified successfully.
Notes: NETCONF uses SSH to implement secure transmission and uses Remote Procedure Call (RPC) to implement communication between the client and server.

## Slide 32: YANG Language Overview
Yet Another Next Generation (YANG) is a data modeling language that standardizes NETCONF data content.
The YANG model defines the hierarchical structure of data and can be used for NETCONF-based operations. Modeling objects include configuration, status data, remote procedure calls, and notifications. This allows a complete description of all data exchanged between a NETCONF client and server.
A data model is an abstraction and expression of data features.
A model is an abstraction and expression of things.
Name, gender, height, weight, age, skin color...
Person
Router
Interface, routing protocol, IP address, routing table...
Notes: YANG originates from NETCONF but is not only used for NETCONF. Although the YANG modeling language is unified, YANG files are not unified.
YANG files can be classified into the following types:
  Vendor's proprietary YANG file
  IETF standard YANG
  OpenConfig YANG
The YANG model is presented as a .yang file.
The YANG model has the following characteristics:
  Hierarchical tree-like structure modeling.
  Data models are presented as modules and sub-modules.
  It can be converted to the YANG Independent Notation (YIN) model based on the XML syntax without any loss.
  Defines built-in data types and extensible types.

## Slide 33: YANG and XML (1)
A YANG file is loaded on the NETCONF client (such as the NMS or SDN controller).
The YANG file is used to convert data into XML-format NETCONF messages before they are sent to the device.
list server {
key "name";
unique "ip port";
leaf name {
type string;
}
leaf ip {
type inet:ip-address;
}
leaf port {
type inet:port-number;
}
}
YANG file
+
=
<server>
<name>smtp</name>
<ip>192.0.2.1</ip>
<port>25</port>
</server>
<server>
<name>http</name>
<ip>192.0.2.1</ip>
</server>
<server>
<name>ftp</name>
<ip>192.0.2.1</ip>
</server>
XML
Data
name="smtp"
ip=192.0.2.1
port=25
name="http"
ip=192.0.2.1
port=
name="ftp"
ip=192.0.2.1
port=

## Slide 34: YANG and XML (2)
A YANG file is loaded on the NETCONF server (such as a router or switch).
The YANG file is used to convert received XML-format NETCONF messages into data for subsequent processing.
list server {
key "name";
unique "ip port";
leaf name {
type string;
}
leaf ip {
type inet:ip-address;
}
leaf port {
type inet:port-number;
}
}
YANG file
+
Data
<server>
<name>smtp</name>
<ip>192.0.2.1</ip>
<port>25</port>
</server>
<server>
<name>http</name>
<ip>192.0.2.1</ip>
</server>
<server>
<name>ftp</name>
<ip>192.0.2.1</ip>
</server>
=
XML
name="smtp"
ip=192.0.2.1
port=25
name="http"
ip=192.0.2.1
port=
name="ftp"
ip=192.0.2.1
port=

## Slide 35: Telemetry Overview
Telemetry, also called network telemetry, is a technology that remotely collects data from physical or virtual devices at a high speed.
Devices periodically send interface traffic statistics, CPU usage, and memory usage to collectors in push mode. Compared with the traditional pull mode, the push mode provides faster and more real-time data collection.
Request CPU usage 1.
Time 1, usage 1
Request CPU usage 2.
Time 2, usage 2
Request CPU usage 3.
Time 3, usage 3
T < 1s
Subscribe to the CPU usage.
Period: 1s
Time 1, usage 1
Time 2, usage 2
Time 3, usage 3
Time n, usage n
T > 5 min
"Subscription and push"
"Pull"
Telemetry supports
data collection
at the level of subseconds.
SNMP
Telemetry
Notes: There is also a view in the industry that SNMP is considered as a traditional telemetry technology, and the current telemetry is referred to as streaming telemetry or model-driven telemetry.
Telemetry packs the data to be sent, improving transmission efficiency.

## Slide 36
(Single) On an SNMP-based network, which of the following runs the management process to manage the managed devices? ( )
  NMS
  Agent process
  MIB
  SNMP
(Single) In SNMPv1, which of the following operations is used by a managed device to report traps? ( )
  Get-Request
  Set-Request
  Trap
  Response
Notes: A
C

## Slide 37
YANG is a data modeling language. ( )
  True
  False
Telemetry supports data collection at the level of subseconds. ( )
  True
  False
Notes: A
A

## Slide 38
With the development of network technologies, more and more network management and O&M methods are available. The common methods are as follows:
  CLI mode or web system
  SNMP
  Huawei iMaster NCE's intelligent O&M platform (covering management, control, and analysis)